## Slide 1: Data Drive Fracture Mechanics: Discovering Elastic Constants and Failure Criteria using PINNs
Thomas Allard
Samantha Walker
April 26, 2022

## Slide 2: Outline
Background – Fracture Mechanics
Input Data – Abaqus Simulations
Background – PINNs
Elastic PINN
Fracture PINN
Conclusions
References

## Slide 3: Background
Stress intensity factor  energy release rate
Displacement control is stable for brittle crack propagation

## Slide 4: Input Data – Abaqus Simulations
Abaqus finite element (FE) software has benchmark simulations for mode I fracture using the extended finite element method (XFEM).
XFEM is a promising capability for simulating the fracture and failure behavior of a solid material.
Displacement is applied to single edge notch tension (SENT) specimen. The right edge is fixed in the x-direction.
The crack (of initial length a) propagates when stress reaches a limit value of
u
u
a = 300 mm
h = 1500 mm
W = 3000 mm
u = 1 mm
Elastic parameters
E = 210 GPa
ν = 0.3
Fracture criteria
= 220 MPa
= 42.2 N/mm
Mode I fracture energy release rate
Elastic Modulus
Poisson’s Ratio
Max tensile stress

## Slide 5: Input Data – Abaqus Fracture
a = 300 mm
h = 1500 mm
W = 3000 mm
u = 1 mm
Default mesh, 2655 elements and 2760 nodes

## Slide 6: Input Data – Abaqus Elastic
Before developing a PINN for the fracture problem, we decided we would try a simpler problem.
Crack removed, all other dimensions and simulations parameters were kept the same.
Pure uniaxial stress state!
h = 1500 mm
W = 3000 mm
u = 1 mm

## Slide 7: Input Data Extraction and MGMT
Abaqus/Python API to extract results from Abaqus output database (ODB)
Xarray “DataArray” for each timestep  stack into “DataSet”
  Fields:

## Slide 8: Background - PINNs
General – borrow from old slides
Sciann
  Why??? Lol Yang *shrugs*  they actually have great examples! We used
  https://github.com/sciann/sciann-applications
Data – (maybe move to end of Abaqus discussion)
  Abaqus output database (ODB) extraction
  Used xarray data formats (DataSets and DataArrays) to conveniently store and call simulation data, netcdf file
Hyperparameters
  Started from sciann-applications
  Tested different normalizations

## Slide 9: Elastic PINN
Some outputs and plots
Troubles! 

## Slide 10: Fracture PINN
Technically no trouble! (cuz we didn’t get here yet lol)
Ambitious goals

## Slide 11: Conclusions
Why NNs so hard 

## Slide 12: References